## Slide 2
Current, resistance and electromotive force
Current
Current is a concept with wide spread applications describing the rate of flow of some quantity that can be:
-Throughput of cars per time interval:
-water volume coming out of a hose per time interval:

## Slide 3
Electric current:
Motion of charge from one region to another quantified by
Currents in conducting materials:
Simple classical description (Drude model) to introduce basic relations
Classical equation of motion:
friction due to the scattering
processes
electric force F=qE
accelerating the charge q=-e0
where vd is the
drift velocity
superimposed to the random thermal velocity
Almost random motion with average speed of 106m/s
However, drift velocity in x-direction
very slow of the order of 10-4m/s
x

## Slide 4
Switching off the electric field
Relaxation to the thermal velocity within
relaxation time 
Stationary state in an electric field:
0
dQ=q dN
dV=Adx
where

## Slide 5
It is important to separate out which results are model dependent and which are general expressions
general expression for current density vector
Note: j is a vector, the current I is a scalar.
Some remarks:
Conventional current
Positive charges in positive E-field
Experience force in positive x-direction
and define the positive current direction
Negative charges in positive E-field
experience force in negative x-direction
and produce likewise positive current
-direction of current flow
Note also, the orientation of j does not depend on the sign of the charge

## Slide 6
-The SI unit of current
1A=1 C/S
after André Marie Ampère
Resistivity
In our simple Drude model for metallic conductivity we found
with conductivity
a material dependent constant
The reciprocal of conductivity is resistivity
Resistivity defined as
In general
if  is constant, meaning independent of E we call that Ohm’s law
after Georg Simon Ohm

## Slide 7
We start from
Alternative formulation of “Ohm’s law”
I
A
Current density:
L
E
V
Voltage drop V=E L
Note: in the most general case when materials are not isotropic,  and  are
not scalars
and integrate current density over

## Slide 8
with
the resistance
Note: this equation is often called Ohm’s law. Again, Ohm’s law is the fact that R is in good approximation independent of V for metals.
Table from textbook Young & Freedman

## Slide 9
Which of the following statements below is correct?
Clicker question
1) Ohm’s law is a fundamental law of nature
2) Ohm’s law is not a law in a strict sense but an approximation
which holds very well for metals
3) Ohm’s law is expressed by V=R I

## Slide 10
Current-voltage relationship for
A resistor that obeys Ohm’s law
I
V
slope=1/R
A resistor with a nonohmic characteristic
such as a semiconductor diode
I
V

## Slide 11
Resistivity and Temperature
T

Scattering of electrons: deviations from a perfect periodic potential
Impurities: temperature independent imperfection scattering
phonon scattering
Matthiessen’s rule:

## Slide 12
In the linear regime we write
Table from textbook Young & Freedman
Simple approach to understand
for T>>ӨD
Remember Drude expression:
scattering rate
#of scattering centers/volume
scattering cross section
scattering cross section
Fermi velocity of electrons:

## Slide 13
Note, temperature dependence of resistivity of non-metals can be very different
Typical semiconductor, e.g., Si
Superconductor
Flowing fluid analogy and interpretation of resistance
See also
http://hyperphysics.phy-astr.gsu.edu/hbase/electric/watcir2.html
In both cases
R L
length of hose
length of wire
Also: R increases for narrow water hose
but the dependence is not 1/A

## Slide 14
Consider the situation Iwire=Ibulb but Rwire=0.5 and Rbulb=140
Iwire
100m of 12-gauge Cu wire
Rwire=0.5
Ibulb
Rbulb=140
@ operation T
Potential difference V=IR across light bulb >>V across wire
Each charge carrier loses more potential energy in the bulb
in comparison to the wire
This lost potential energy in the light bulb is converted into light and heat

## Slide 15
Color code for resistors and symbols in circuit diagrams
Table from textbook Young & Freedman
Symbols used in circuits
ideal conducting wire with R=0
resistor with non-zero resistance R
Example
R=
5
7
00
=5.7k 10%

## Slide 16
Electromotive force
Let’s consider the flowing fluid analogy again
Water intake
at low pressure
low pot. energy
High pressure
Pump increased
potential energy
of the water.
Water moves in the direction
of decreasing pot. Energy,
direction of gravitational force
In the pump water flows against
the gravitational force
Electric circuit
device similar to water pump where charge is moved “uphill”
from lower to higher potential energy.
What makes the electric current flow “uphill” is called electromotive force, emf

## Slide 17
Every complete circuit with a steady current must include some device
that provides emf
Like the electric potential, emf (we use the variable ) is an energy per charge
If a battery has an emf of
battery does 12 J of work for every Coulomb
of charge passing through it to increase the
potential energy of the charge by 12J
Examples of sources of emf:

## Slide 18
Terminal at higher
potential
Let’s have a look at an ideal source of emf in the force picture
+
-
+
Terminal
at lower potential
Va
Vb
E
nonelectrostatic
force moving the charge slowly from b to a
does work
For an ideal source of emf

## Slide 19
Let’s integrate the ideal source into a complete circuit
Terminal at higher
potential
+
-
+
Terminal
at lower potential
Va
Vb
E
wire with non-zero
resistance R
E
E
E
I
I
I

## Slide 20
Let’s integrate a real source into a complete circuit
Terminal at higher
potential
+
-
+
Terminal
at lower potential
Va
Vb
E
Charge moving through real source
experiences resistance (a friction force)
if internal resistance, r, ohmic
Terminal voltage of a source with internal resistance

## Slide 21
Potential changes around a circuit
We know: net potential energy change for a charge making a round trip is zero
We can express this by rearranging
into
The sum of all potential drops and emfs around a loop is zero
http://hyperphysics.phy-astr.gsu.edu/hbase/electric/watcir2.html#c2

## Slide 22
An example for
for a circuit with a real source
From textbook Young & Freedman