## Slide 1
Kirchhoff’s rules
How to find this equivalent resistance in most general cases
Rules for resistors in series and parallel very useful, but:
Not all resistor networks can be reduced to simple combinations of series and parallel circuits such as this one
Kirchhoff’s rules
http://en.wikipedia.org/wiki/Gustav_Kirchhoff

## Slide 2
2 fundamental laws of nature allow to deduce Kirchhoff’s rules
Conservation of charge
Kirchhoff’s junction rule
At any junction* in a circuit the sum of the currents into any junction is zero
*Junction (also called node):
is a point in a circuit where three or more conductors meet
example for a junction
not a junction

## Slide 3
Kirchhoff’s junction rule and the flowing fluid analogy
I1
I2
I3=I1+I2
Note: obviously we have to carefully identify the signs of the partial
currents when applying the junction rule I1+I2+I3=0
Sign convention needed:
We count current flowing into a junction (I1,2 in our example above) positive and those flowing out (I3 in our example above) negative

## Slide 4
Electrostatic force is conservative
Potential energy and potential are unique functions of position
Kirchhoff’s loop rule
the sum of the potential differences in any loop (including those with emfs) is zero

## Slide 5
Sign convention and examples
We first investigate an elementary simple network
1
R
Let’s start by labeling all quantities
2
Let’s choose a direction for the current and a direction we choose to go through the loop, e.g., clockwise
3
Consider yourself a positive charge traveling the loop
4
In this simple example there are no junctions
We only need the loop rule here
+
+
-when we flow with the current through R we loose potential energy
-when we flow through the source of emf from – to + we gain potential energy
-when we flow with the current through r we loose potential energy
as seen before
I

## Slide 6
Can we travel in the opposite direction and get the same result
R
+
We keep the current direction but travel against the current
-when we flow against the current through R we win potential energy
-when we flow through the source of emf from + to - we loose potential energy
-when we flow against the current through r
we win potential energy
I

## Slide 7
Now an example that involves the junction and loop rule together
Example: charging a battery from our textbook Young and Freedman
The direction of this
current is our choice
Goal:
-determine unknown emf of the run-down battery
-determine internal resistance r of the 12V power supply
-determine the unknown current I
We will need 3 equations
for the 3 unknowns
Travel-directions we choose to go through the loops

## Slide 8
We apply the junction rule to point a
Junction rule at point a: +2A+1A-I=0
1
I=3A
Loop rule for outer loop 1:
2
Loop rule for loop 2:
3
The minus signs says that the polarity of the battery is opposite to what we assumed in the figure
It better is opposite, because who would try to jumpstart a car by connecting terminal of different sign, not a good idea!
Loop rule for loop 3 can be used to check :
4

## Slide 9
Example of a complex network
which cannot be represented in terms of series and parallel combinations
I4
I5
I6
direction of I3 is an assumption
which we may or may not
confirm throughout the calculation
Goal: Finding all 6 unknown currents and the equivalent resistance
1
Junction rule at c:
2
Junction rule at a:
3
Junction rule at b:
We could apply the junction rule at d
No new eq. just confirming

## Slide 10
We need 3 additional equation
applying the loop rule for 3 loops
1
loop1:
2
loop2:
3
loop3:
We could apply the loop rule for the remaining loop
No new eq. just confirming
From 3:
into 1:

## Slide 11
Together with eq. 2 we get
minus sign indicates that I3 flows opposite to our assumption in the figure
Total current through the network
Equivalent resistance
Check the result with remaining loop:

## Slide 12
What happens to the brightness of bulbs A and B
when bulb C is removed from this circuit?
For simplicity let’s assume A,B and C are identical
Clicker question
1) No change in A, B gets brighter
2) A gets dimmer, B gets brighter
3) A and B get dimmer
4) No change in A, B gets dimmer
5) A and B get brighter

## Slide 13
First case with bulbs A,B and C installed:
The emitted light intensity depends on the dissipated power of each bulk
We calculate total resistance
Check: total dissipated power
Second case with C removed:
(total resistance increased)
(total current decreased)
(voltage drop
across A decreased)
(bulb A gets dimmer)
(voltage drop
across B increases)
(bulb B gets brighter)
(reduced because current goes down while V=const)